## Slide 1
Rev.07.9
Firebird W

## Slide 2: Firebird - Specifications
Basic performance
  XY accuracy:
        ± 2.0m @ 3
  Angular accuracy:
        ± 0.01 @ Cpk 1.33
  Z accuracy:
        ± 1m @ Cpk 1.33
  Co-planarity: 3m over 33mm
  Cycle Time < 2.0 sec
Process capabilities
  Bond pedestal temperature:
        Max 200C ± 5C
  BH nozzle temperature:
        Max 400C ± 2C
        Ramp up rate > 450C/sec (Die size<14x13mm)
    > 125C/sec (Die size > 14x13mm)
        Cooling rate < -80C/sec (Die size<14x13mm)
    < -57C/sec (Die size > 14x13mm)
Bond force: 0.1N ~ 10N ~ 300N
        Accuracy: ± 5% @ Cpk 1.33
  Inert environment:
    O2 level < 100ppm
  Integrated jet dispenser (option)
  Flux Dipping (option)
  Multi-Chip
Page 2
2016-09-07

## Slide 3: Specifications: Die and Substrates Media
Die size
        2x2mm ~ 33x22mm
        Min thickness: 0.04mm
Die media
Tape and reel
          Sizes: 8,12,16,24,32,44,56mm
          Reel diameter: 330mm
Waffle pack
        2” x 2” or 4” x 4”
Wafer Frame 8”,12” (flip/non-flip)
Firebird W Substrate
  Wafer
    Max Diameter 310mm x 2mm thick
Firebird S Substrate
  Singulated substrate
        10mm ~ 110mm
        Max aspect ratio: 3
  Strip substrate
    50 x 125mm ~ 125 x 250mm
    Min thickness: 0.17mm
  Substrate media
    JEDEC tray
    Strip on Carrier with magnetic captive frame
    Boat Carrier
Page 3
2016-09-07

## Slide 4: Configuration for Intel Chip to Wafer
Main Bonder
    Firebird W for 12” wafer substrate (1BH 1BS)
Substrate Input
    EFEM  if manual load unload is acceptable, we may not need this.
Die input
    WFM
    TnR
    Waffle Pack  please confirm if need this
Operation Unit
    Pulse Heater 14mmx14mm
    Flux Dipping unit LDU-X
            May consider re-use the LDU-X demo unit that we are going to ship to Chandler
            Please advise if pre-applied flux spray is an option for the process.
              If Intel has a spray machine that can accept input wafer from EFEM.
Page 4
2016-09-07

## Slide 5: Configuration for Intel C2W
    Collaterals
      Die size
        Sample 1: 7.3mmx7.3mm x thickness? 8” wafer on 12” wafer ring?
        Sample 2: 12.86586mm x 13.47469mm x thickness? 12” wafer on 12” wafer ring
      WFM
        Ejector Kit (to be defined)
        Flip Arm nozzle, Pick nozzle
      Firebird
        12” ceramic pedestal (assume universal design for 8” and 12” wafer)
        BH Nozzle (provide by Intel / may consider make Si one for temporary use)
        DPA nozzle
        If flux dipping
          DPA nozzle for flux dipping
          Die holder on DTA
          Flux plate (please advise cavity depth required)
Page 5
2016-09-07

## Slide 6: Configuration for WFM + Firebird W (with TnR, 14mm heater) + EFEM
4090
1600
1560
930
1450
2500
3850
2500
Page 6
2016-09-07

## Slide 7: Configuration for WFM + Firebird W + EFEM
Front view
2450
1680
2200
Page 7
2016-09-07

## Slide 8
END